## Slide 1: Improved modelling of the JEM-X collimator
SDAST meeting #29
DSRI, August 2004
Niels Lund

## Slide 2: Detailed modelling of the JEM-X collimator (to improve off-axis response)
Three new effects are considered:
Tilt of the collimator lamellae (independently for the Y and Z lamellae – 2 parameters)
Non-flatness of lamellae (1 parameter)
Spherical deformation of the collimator (1 parameter)

## Slide 3: Optimization method
Data from observations of the Crab in orbit 43-44, 102 and 170 have been used.
Instrument parameters were varied, one at a time.
A search for a minimum in the variance of the Crab intensity variations as function of off-axis angle were sought.

## Slide 4: The 16 instrument parameters involved in the optimization
7.05 7.05 coll_pitch // nominally: 7.05 mm
0.45 0.375 coll_width // nominally: 0.45 * 0.5 mm
3393.0 3393.0 mask_height // nominally: 3401 mm
// Common-X is the direction from JEM-X2 to JEM-X1
-0.03 180.00 alfa // angle betw. Mask-X and Common-X
-0.17 180.0 beta // angle betw. collim.-X and Common-X
0.00 179.97 gamma // angle betw. M-strip-X and Common-X
-0.05 0.0 xshift mm // X shift of microstrip wrt collim.
3.5 3.50 yshift mm // Y shift of microstrip wrt collim.
-0.2 -0.325 c_tiltx mm // X tilt of collimator walls
0.2 -0.01 c_tilty mm // Y tilt of collimator walls
1.0001 1.0035 coll_curv // collim. curvature (1.0 = flat collimator, >1.0 = high in the center)
1.0002 1.0009 mask_scale // scale (hexa_dim & mask_height)
// Parameters for transf. from JEM-X to sky directions
0.00015 0.0003 phase2 // twist of Common-X wrt star-tracker
-1.10 -0.84 offX // X-offset (pixels in 255x255 image)
-2.50 -2.37 offY // Y-offset (pixels in 255x255 image)
+ rms values for the position uncertainty in four energy bands.

## Slide 5: Crab flux vs off-axis angle (model adjusted to revs. 43-44)

## Slide 6: Application of improved collimator model to imaging
The improved collimator model has been implemented into the midisky IROS software.
The result is that the strength assigned to the sources have increased by 20 to 50%. (The weaker sources normally shows the largest increases).
The number of spurious source candidates (>5 ”sigma”) are reduced by 10 %.

## Slide 7: Flux extraction (3 methods)
1) Spectral extraction software: Take signal in ”illuminated” pixels and subtract corresponding signal from ”shadowed” pixels. (According to ”best” source model).
2) IROS imaging software: Fit source strength with ”best” source model.
3) Image analysis Count events in image peaks
(normalization problems not yet adressed)

## Slide 8: Crab flux vs off-axis angle Different extraction methods

## Slide 9: JEMIROS status
OSA4 installed on laptop
Paul Connells JEMIROS updated to match midi_b5
Current midisky (mb8) cleaned for ’print’ statements, ’exit(0)’ statements replaced by error returns and replacement of all common parameters with struct parameters is in progress.

## Slide 10: Science Results & Issues
Sgr A* Galactic Centre (Goldwurm et al.)
IGR 19140+0951 New source (Hannikainen et al.)
3EG 1736-2908 EGRET source (Di Cocco et al.)
1E 1841-045 Anomalous X-ray Pulsar (Kuiper et al) ***
Core Programme during AO-3
1.3 Ms Galactic Centre. 2 x 5 x 5 pt dither (at 45 deg) - 2.17 deg spacing
1.4 Ms Scutum Arm 10 x 5 points, 2.17 deg spacing
0.8 Ms Norma Arm 10 x 5 points, 2.17 deg spacing
1.3 Ms Galactic latitude scan 5 x 16 points 2.0 deg spacing
? Ms Galactic Plane Scans every 12 days, step size 7 deg, |b| < 6.45 deg
1.0 Ms Deep Extragalactic Survey 5 x 12 pointings, 2.17 deg spacing. (Virgo, 3C273, 3C279)

## Slide 11: Galactic Center - 2003 GCDE

## Slide 12: Galactic Center - 2004 SgrA
PI: A. Goldwurm